## Slide 1: Unit 5, Lesson 12 How Memory Works
AOIT Computer Systems
Copyright © 2008–2013 National Academy Foundation. All rights reserved.

## Slide 2: RAM is high-speed temporary memory
  Holds currently used data for the processor and operating system
  Allows both reads and writes
  Accesses data in electronic blocks that the system can access in any order
The more RAM, the better
A RAM module stores bits of data in capacitors. (A bit is always either 1 or 0.)

## Slide 3: Unlike memory, storage is permanent
Hard drives
Solid-state drives
Optical drives: CDs and DVDs
What types of storage are shown in these images?

## Slide 4: ROM is permanent read-only memory
Read-only memory (ROM):
Stores data even when the computer is powered off
Holds information that is prerecorded and unchangeable
Types of ROM chips:
EPROM
EEPROM
What information do you think is stored even when the computer is off?

## Slide 5: Cache memory stores data in transistors built into the processor
The fastest and most expensive memory in a PC
Acts like a buffer between RAM and the processor
Predicts what data will be requested next and retrieves it from RAM
The first place the operating system looks when it needs to retrieve data

## Slide 6: There are three levels of cache
L1 | Smallest (holds the least data) | Fastest
L2 | Larger than L1 | Fast because it is on the processor in newer, high-end systems
L3 | Largest | Slower because it is on the motherboard
Each level of cache is bigger than the previous level and contains copies of it.

## Slide 7: Cache is faster but more expensive than RAM
  Cache requires more transistors than RAM to store a single bit of data, and the circuit is more complex.
  The more transistors, the more expensive the chip.
  Hot transistors need heat sinks, which also increase the cost.

## Slide 8: Disk cache holds overflow data in hard drives
Disk cache is the memory in a hard drive that acts as a buffer between the computer and the physical hard drive.
It holds data that has recently been read from the disk.
Write-back cache is updated frequently, when necessary.
Write-through cache caches data only for read operations.

## Slide 9: Virtual memory stores overflow data from RAM on the hard drive
Hard drives have reserved space for virtual memory.
When RAM is full, data that is requested is swapped in and out of virtual memory.
Virtual memory is 1 million times slower than RAM.
Swapping data in and out of virtual memory too often results in disk thrashing.
Performance is slow on a hard drive that is over 80% full because there is limited space for virtual memory.

## Slide 10: You can troubleshoot memory problems
Problem | Action
Poor performance | Check the activity light on the hard drive
Error messages | Shut down some applications or add more memory
Sudden and unpredictable crashes | Remove bad memory modules
Corrosion | Match module connector materials to memory connector materials

## Slide 11: Use the right memory for best performance
Many components in a computer system require their own memory in order to store data.
Knowing which type of memory works best in different parts of the PC helps you achieve top performance in your system.
Which type of memory does each image represent?